## Slide 1: Quest for Dark Matter by direct detection experiments with noble liquids
Hiroyuki Sekiya
ICRR & Kavli-IPMU, University of Tokyo
from XMASS collaboration
Dec. 12 2013
KMI International Symposium 2013(KMI2013)

## Slide 2: Contents
Principle of direct detection
  Direction insensitive searches
Detection technologies with liquid noble gas = noble liquid
  Review of 2 phase detectors
  Review of single phase detectors
    XMASS
    Liquid Xe TPC
Future noble liquid detectors
Total 40 pages

## Slide 3: Principle of WIMP Direct Detection
Particle physics × Astrophysics
(cross section) (flux)
Both cross section and flux must be studied, but…
WIMP-nucleus cross section
WIMP density
WIMP velocity distribution

## Slide 4: Astrophysics -The model-
“Standard halo model”
NASA/COBE Project
MNRAS 211(2000) 361
Bulge
Disc
Sun
Dark Halo
Collision-less Boltzmann equation
Maxwell distribution

## Slide 5: Astrophysics -Recent N-body simulations-
Density
Velocity distribution
8.5kpc
arXive;0907.0018
JCAP 02(2010) 012
Density profile of the halo
in the galactic plane
3GeV/cm3
1GeV/cm3
0.3GeV/cm3
0.1GeV/cm3
JCAP 02(2010) 030
Suggestion of deviations from the Maxwell
distribution, particularly at high velocities.
→Impact on Light WIMPs
Direction sensitive search
Maxwellian
simulation
1s

## Slide 6: Particle physics after LHC
SUSY is still attractive, but it goes far…
  Scattering cross sections on nucleons sc-n is now down to ~ 10-48 cm2
arXive:1311.0678
cMSSM
NMSSM
Eur. Phys. J. C72(2012) 2243

## Slide 7: WIMP-Nucleus elastic scattering
Cross section
Recoil energy
In this talk
only SI is focused.
I love Fluorine!
sc-n

## Slide 8: Expected detection rate
Integration over the velocity distribution (SI)
For different Nuclei
Ton scale is necessary. Heavy nuclei/Light WIMPs are easier for us.
For different WIMP mass
sc-n=10-48cm2
Mc=100GeV
Heavy nuclei
Light nuclei
Heavy WIMP
Light WIMP
sc-n=10-48cm2
Target:Xe

## Slide 9: Direct Search Experimental Challenge
WIMP nuclear recoil signal is:
  Low rate (<1 events/ton/year)
  Small energy (<10keV, actual observed is less)
  Similar observed exponential spectrum to many background signals
Detection technique must be:
  Extremely low background
  Low threshold
  Large mass
It’s better to be
  Position sensitive for fiducalizaition
  Discriminating between WIMPs/n and g/b
  Directional
As we already see

## Slide 10: Technologies in 2003
Y.Ramachers
Nucl. Phys. B (proc. Suppl.) 118(2003)373
Notes: 2000年との比較をしてしまえ！ そしてphonon に×つける。 ＭＡＳＳの問題 resolutionが有利と思われたがいらない！

## Slide 11: Technologies in 2013
CRESST-I
CUORE
Tokyo
CRESST
CUORE
ROSEBUD
DAMA,LIBRA
NAIAD
XMASS
DEAP,CLEAN
DM-ICE
ZEPLIN
XENON
LUX
DarkSide,
WARP, ArDM,
IGEX
GENIUS
CoGENT
CDEX
DAMIC
TEXONO
CDMS, EDELWEISS, SuperCDMS, EURECA
Tracking
DRIFT
NEWAGE
DMTPC
MIMAC
emulsion
Superheated liquid
COUPP
PICASSO
SIMPLE

## Slide 12: Direct searches @ Earth
Baudis SUSY2013

## Slide 13: Current Status
SI WIMP-nucleon cross section limit as of Nov 2013
  The best is LUX, reaches 10-46cm2.
  Top 3 are all two phase Xe detectors
XMASS
LUX
XENON100
CDMS Ge
XENON10
EDELWEISS
LUX
XENON100
XENON100
ZEPLIN-III
CDMS-II
arXiv:1310.8214
Phys. Lett. B 719 (2013) 78

## Slide 14: Noble liquid detector
scintillation detector / ionization detector
Baudis SUSY2013
Aprile Phys. Rev. Lett 97(2006)
Transparent to their own light
LXe

## Slide 15: Why is noble liquid strong for WIMP?
Large mass/scalability especially Ar ←cost
Large mass number especially Xe
→Passive BG rejection: self shielding by fiducalization
Large light yields→low threshold
Purification→low BG
NJT Smith ICRC2013T
Noble gas interaction process
Both scintillation and ionization are detectable.
Excitation/ionization ratio provides the electron/nuclear recoil separation
→Active BG rejection

## Slide 16: How to use noble liquids; 3 concepts
Single (liquid) phase
  Just as scintillators
    Through the recombination process, in a sense, it is also sensitive to Ionization.
    Singlet/triplet ratio difference between nuclear/electron recoil event ←possibility of PSD
  TPC to measure ionization directly
    By applying electric field, electrons produced by ionization are collected. These can be observed via charge amplification or proportional scintillation by high electric field.
Two phase (liquid+gas)
  TPC same as single phase,
    If electrons are extracted from liquid phase to gas phase, it becomes easier to get the charge amplification /proportional scintillation by high electric field.

## Slide 17: Single phase scintillator
S1
PMT array
Time
S1
PSD?
This concept has realized recently.

## Slide 18: Single phase TPC
+HV
-HV
e-
S2
E
e-
e-
S1
E
S1
S2
+HV
Charge
e-
e-
e-
Time
S1
S2
The original concept, but has not realized yet.

## Slide 19: Two phase TPC
+HV
-HV
e-
E
e-
e-
S1
S2
Time
S1
S2
Realized earliest and well-established with success

## Slide 20: Liquid Xe/Ar TPCs
Based on
N.J.T. Smith ICRC2013
L. Baudis SUSY2013
LUX@SURF
XENON100@LNGS
PANDA-X
@CJPL
ArDM
@Canfranc
Darkside
@LNGS
350kg total
118kg FV
122 2’’ PMTs
Continues
data taking
till 2015
161kg total
50kg FV
242 1’’ PMTs
Continues
data taking
125kg total
25kg FV
143 1’’ PMTs
37 3’’ PMTs
Started
data taking
850kg total
100kg FV
28 3’’ PMTs
In commissioning
Will start
data taking in 2014
50kg total
33kg FV
39Ar depleted
38 3’’ PMTs
Started
data taking

## Slide 21: Event examples in two phase detectors
1.5keV gamma in LUX
D. McKinsey, R. Gaitskell Oct30 2013
S1
S2
Drift time (ms)
PMT channel
9keV recoil in XENON100
Top PMT
Bottom PMT
L. Baudis SUSY 2013
4p.e..
645 p.e.
←32 e-

## Slide 22: Electron/nuclear recoil separation power
XENON100 case
N. Priel SUSY2013

## Slide 23: DM search results
LUX 85 days
XENON100 225 days
D. McKinsey, R. Gaitskell Oct30 2013
N. Priel SUSY2013

## Slide 24: Liquid Xe/Ar scintillators
XMASS-1@Kamioka
miniCLEAN@SNOLab
DEAP3600@SNOLab
835kg total
100kg FV
642 2’’ PMTs
Refurbished
Started new data taking
500kg total
180kg FV
LNe for solar neutrino
Under construction
Will start data taking in 2014
3.6 ton total
1 ton FV
255 8’’ PMTs
Under construction
Will start data taking in 2014

## Slide 25: XMASS must be extremely clean
10m x f10m water shield for external BG
Made of pure materials
    Development of low BG PMTs
Xe purification technologies
    Distillation system
Photo coverage 62.4%

## Slide 26: Clean PMT
YEAR | 2000 | 2002 | 2009
Model | Prototype | R8778 | R10789
Material:Body | glass | Kovar | Kovar
QE | 25% | 25% | 27-39%
RI: |  |  | w/ PMT base
U [mBq/PMT] | 50 | 18±2 | 0.70±0.28
Th [mBq/PMT] | 13 | 6.9±1.3 | 1.51±0.31
40K [mBq/PMT] | 610 | 140±20 | 9.10±2.15
60Co [mBq/PMT] | <1.8 | 5.5±0.9 | 2.92±1.61
XMASS PMT HISTORY
Clean PMT Base has also been developed.
→LUX
Notes: R10789 achieved 1/10 reduction of radioactivity level of R8778

## Slide 27: Xe Distillation System
1 ton LXe = 170 m3 gas Xe Process speed: 4.7kg/hr → 10 days
Confirmed Kr < 2.7ppt by API-MS
4m
 | Boiling point (@0.2MPa)
Xe | 178K
Kr | 140K~150K
Astoparticle Physics 31, (2009) 290
Commercial “pure Xe” contains ~0.1ppm Kr
  85K / K = 1.2×10-11 t =10.8 year, Qβ = 687keV
  5 order reduction was indispensable.
We established
Xe purifiaction
by distillation
→XENON
Notes: For internal BG reduction

## Slide 28: Detector Response
Highest LXe scintillation yields:
14.7p.e./keVee
Lowest threshold: 4hits→0.3keVee
Top PMT
manipulator
Calibration spectrum
real data
simulation
122keV
136keV
59.3keV of W
~4% rms
real data simulation
Reconstructed vertex
57Co
total photoelectrons
-1.4 cm r.m.s. @ z = 0
-1.0 cm r.m.s. @ z = ±20 cm
NIM A 716 (2013) 78
Notes: Thanks to the High QE, coverage, Xe purity, Highest! LY.

## Slide 29: Unexpected BG
BG is 2 order higher than that had been expected.
counts/day/p.e.
total photoelectrons
GORE-TEX?
238U & 210Pb of PMT Al seal
expected BG (PMT & components)
Major origin of BG was considered to be g from PMTs, but the observed data seemed to have additional surface contamination.
  Aluminum sealing parts for the PMT (btw metal body and quartz glass) contains 238U and 210Pb (>5keV)
  GORE-TEX between PMT and holder is suspicious below 5keV.
Data
BG simulation
~1MeV(60Co peak)
~5keV

## Slide 30: XMASS Full Volume: Low BG w/o PID
Although extra BG sources were found, XMASS BG level is still competitive w/o rejecting electron recoil events.
  XMASS has a competitive sensitivity to Light WIMPs
XMASS full volume 5591.4kg days
Evens/kg/day/keV
E. Aprile, 2010
Princeton

## Slide 31: Light WIMPs
XMASS
LUX
XENON100
CDMS Ge
XENON10
EDELWEISS
Set an upper limit on the WIMP-nucleon cross section for WIMPs with masses below 20GeV w/o PID and excludes part of the parameter space allowed by DAMA
  Phys. Lett. B719 (2013) 78
WIMP mass [GeV/c2]
18GeV
12GeV
7GeV
DAMA 5s
10-40
10-41
10-42
10-43
10-44
data
0
0.5
1
1.5
2
1
2
3
4
5
/kg/keVee/day
sWIMP-n cm2
[keVee]

## Slide 32: XMASS-1 Refurbishment for Background reduction
Countermeasures
  PMT+Cu surface cleanup
  Remove GORE-TEX
  Cover PMT Aluminum seal
    Cu ring around aluminum seal
    Electropolished Cu cover above Cu rings

## Slide 33: Refurbishment
Has just resumed data taking… looks nice!
before
after

## Slide 34: Single phase TPC
Before the two phase detector realization, there were
many studies about the charge amplification and the proportional scintillation in single phase LXe.
Derenzo , Phys. Rev. A 9 (1974) 2582
Charge gain ~400
LXe
Miyajima NIM 134 (1976) 403
Charge gain ~100
LXe

## Slide 35: S2 in LXe
Masuda NIM 160 (1979) 247
LXe
LXe
109Cd 22keV was observed
Charge gain &
proportional scintillation
Benetti NIMA 327 (1993) 203
LXe

## Slide 36: Single phase TPC
Spherical LXe TPC
  High electric field in XMASS
  20kV at the center
Masuda,Itow and HS
ParisTPC conf (2012)
E
S1
S2
+HV
Charge
e-
e-
e-
Field
Gas spherical TPC
Giomataris JINST 3:P09007(2008)
HV
(GND)
Will be tested with single
wire in this chamber

## Slide 37: Single phase TPC
S1
Thick GEM in LXe
Detects S1&S2
Detects S1
THGEM 70 kV/cm
Etop = 0, Edrift = 1 kV/cm
RD51 Aug 2013
S1
S2
Thickness 0.4mm
Breskin
ParisTPC conf (2012)

## Slide 38: Near Future Projects How much noble liquids do we need?
To reach ～10-48 cm2
arXiv:1306.3244

## Slide 39: Future Projects (all in water)
Time
LZ
XENON1t
3.5t total
248 3’’ PMTs
In 2015?
x n?
XENON nt
XMASS1.5
5t total
New 3’’
PMTs
DarkSide G2
5t total
LZ = LUX+ZEPLIN
7t total
500 3’’ PMTs
DARWIN
20t LAr
10t LXe
XMASS 2
24t total

## Slide 40: Evolution of Direct Dark Matter Search
Can we realize?
L.Baudis Phys Dark Univ.1(2012) 94
1 events/kg/yr
1 events/ton/yr

## Slide 41: Conclusion
Direct detection experiments have reached the sensitivity of cross section down to 10-46cm2 region with noble liquid technologies.
Next 5 year’s detectors which aim at <10-47cm2 are all using noble liquids.
  Can noble liquids catch Dark Matter?
  Beyond noble liquids, completely new technology will be required?
  SUSY? After LHC upgrade, we may have to go further…

## Slide 42: Extra slides

## Slide 43: The effects of the deviation from Maxwellian
“Standard” vs VL2

## Slide 44: Uncertainties on the relative scintillation yeild
Relative scintillation yield measures quenching of scintillation in nuclear recoils compared to electron recoils

## Slide 47: What makes the WIMP signal?
232 km/s
revolution 30km/s
Sun
DARK HALO
(Maxwell 分布)
Ｖ０＝220km/s
Cygnus
Earth’s motion in the galaxy
Cygnus direction
232 km/s
revolution
30 km/s
Change of Ｒ
Change of

## Slide 48: XMASS Projects…
  Xenon MASSive detector for Solar neutrino (pp/7Be)
  Xenon neutrino MASS detector (double beta decay)
  Xenon detector for Weakly Interacting MASSive Particles(DM)
24t
(10t fiducial)
Ø 2.5m
The ultimate XMASS
Multipurpose low BG experiment with single phase (liquid) Xe
dark matters, neutrinos
neutrinos,
axions
136Xe
Y. Suzuki, hep-ph/0008296

## Slide 49: Solar Axions
XMASS has also sensitivity to solar axions that would be produced by Bremsstrahlung and Compton effects (gaee ) in the Sun through the axio-electric effect in Xe
  N.B. Not gagg through Primakoff effect
Expected flux gaee=10-10 .
JETP Lett., 95, 379 (2012)
arXiv:1206.4142
A. V. Derbin et al.,

## Slide 50: Solar Axions
Same data set as Light WIMP search
No indication of signals. Bound in gaee vs. mass.
Better than any other constraint in 10-40keV.
Better than any other experimental constraint
  Phys. Lett. B724 (2013) 46
Data
Signal MC
Notes: EDELWEISS-II arXiv:1307.1488

## Slide 51: Next step: XMASS-1.5
Inner Ø: 1.5 m
  contains 5 tons of LXe
  fiducial mass 1 ton
Lessons from XMASS-1 New PMT
Still Dark matter detector
Flat photocathode
cannot catch
Plano-concave photocathode
can catch

## Slide 52: XMASS-1.5
Actively being developed w/ Hamamatsu
Effectiveness is verified by MC

## Slide 53: Pure components
RIs of all the components were measured with HPGe and low RI materials were selected.
C1020(OFHC)
SUS304 screws
LEDs
More than 250 components
PMT(R10789)
 | Sum of other components
RI: | Compared w/ 642 PMTs
U | <35%
Th | <35%
40K | <20%
60Co | <20%
RI: | /one PMT
U | 0.70±0.28 mBq
Th | 1.51±0.31 mBq
40K | 9.10±2.15 mBq
60Co | 2.92±1.61 mBq
3 HPGe detectors
in Kamioka

## Slide 54: Quenching Factor/Leff uncertainty

## Slide 55: Xe circulation system
800kg
700L
Liq. Storage
liquid pump
Condenser
360W
gas pump
filters
Calibration line
Cable line
filters
Outer vacuum
1050kg
10 m3
x 2
gas storage
emergency gas pump
100L/min
4 x 180W refrigerator
PTR developed by KEK
evaporator
Water tank
Liquid circulation 5L/min
Gas circulation 30L/min
Notes: We are planing to putfilters to remove Rn, here…

## Slide 56: Water shields for external BG
Active for m, passive for g,n
Liq. Xe
water
X [cm]
y [cm]
10m
10m
with 70 PMTs (20 inch) to detect Cerenkov light
Ex.) Fast n flux @Kamioka mine:
(1.15+0.12) x10-5 /cm2/sec
Assuming all neutron’s energies are
10 MeV very conservatively
5m tank is enough large to shield n and g
< 10-4
count/day/kg
107 n generated
Water purification system
keeps Rn < 1mBq/m3
Notes: THIS PAGE CAN BE SKIPPED
200cm is enough, but it is designed for future large detector.

## Slide 57: U chain Th chain

## Slide 58: Calibration System
Calibration source rod
Source list
OFHC (C1020) rod
source＋holder
(Exchangeble)
adopter (SUS304)
Isotopes | Energy [keV] | intensity [Hz] | diameter [mm]
(1) Fe-55 | 5.9 | 350 | 1.42
(2) Cd-109 | 22, 25, 88 | 800 | 1.42
(3) Am-241 | 59.5 | 485 | 0.15
(4) Co-57 | 122 | 100 | 0.21